## Slide 1: Digital Design with HDL (2019-2020) EcE-41021
Dr. Tin Thet Nwe

## Slide 2: Embedded System
most, based on digital signals
analog sensors
(low-noise amplification,
filtering)
analog actuators
ADC
DAC
success of smart
sensors and actuators
standardized communication buses as the interface
between sensors/actuators

## Slide 3: Embedded System
based on microcontrollers, computers,
application-specific integrated circuits(ASICS) ,or FPGA
Selecting the most suitable technique
  cost, performance, energy consumption, available resources (i.e., computing resources, sizes of different types of memories, or the number and type of inputs and outputs available )

## Slide 4: Target Technology
General-purpose processors and microcontrollers are the best (and some-
times the only practically viable) solution for simple embedded systems with
low computing power requirements.

## Slide 5: Field Programmable Gate Array(FPGA)
developing configurable, custom hardware that might accelerate execution while providing energy savings.

## Slide 6: Difference between FPGA and Microcontrollers
add ( a,b,c)
A=b+c
return
Intel
Core i7
microprocessor
compiler
C code
Microprocess

## Slide 7: Difference between FPGA and Microcontrollers
entity add is
port
(b,c:input unsigned;
a: output unsigned
);
architecture arch of add is
begin
a<= b+c;
end arch;
synthesis
LUT
LUT
LUT
LUT
LUT
LUT
LUT
LUT
LUT
RAM-based lookup tables instead of AND-OR gates to implement combinational logic
an array of configurable logic blocks (CLBs) surrounded by an array of I/O blocks.
Each CLB in the Spartan-3E FPGA contains four slices, each of which contains two 16 x 1 RAM look-up tables (LUTs), which can implement any combinational logic function of four variables.
routing
VHDL code
FPGA chip

## Slide 8
In addition to
distributed logic,
specialized
hardware blocks

## Slide 9: Basic Hardware Resources (FPGA)
basic hardware resources of FPGAs are LBs, IOBs, and interconnection resources

## Slide 10: CAD Tools
Design Entry
Synthesis
Optimization
Simulation
Physical Deisgn

## Slide 11: Nexys4 DDR board(Artix-7™ Field Programmable Gate Array (FPGA) from Xilinx)

## Slide 13: Hardware Description Language
VHDL ( Very high speed integrated circuit hardware description language)
Verilog

## Slide 14: Introduction to VHDL
In the 1980s,rapid advances in integrated circuit technology
industry standard language for describing digital circuits
1987 and called IEEE 1076
1993 and called IEEE 1164
the initial description of the circuit in the form of VHDL code
VHDL compiler translates this code into a logic circuit
integers or characters, data objects in VHDL can be of various types.
BIT , 0 or 1

## Slide 15: VHDL architecture
library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;
entity example is
port(
-
-
-
);
end example;
architecture logic_function of example is
begin
-
-
-
end logic_function;

## Slide 16
The input and output signals in an entity are speciﬁed using the ENTITY declaration
An ARCHITECTURE provides the circuit details for an entity.

## Slide 17: Documentation in VHDL Code
VHDL compiler ignores any text on a line after the ‘- -’.
--This is our test circuit

## Slide 18: Data Objects
Three kinds of data objects are provided: signals, constants, and variables.
Data Object Names
  any alphanumeric character including ‘-’
  legal names are x, x1, x_y, and Byte.
  examples of illegal names are 1x,_y, x__y, and entity.
VHDL is not case sensitive. Hence x is the same as X,

## Slide 19: Data Object Values and Numbers
SIGNAL data objects to represent individual logic signals in a circuit, multiple logic signals, and binary numbers (integers).
The value of a multibit SIGNAL is given with double quotes.
    Example:”0001’, :10101011”
Integers, not using quotes

## Slide 20: SIGNAL Data Objects
SIGNAL ,represent the logic signals, or wires, in a circuit.
SIGNAL signal_name : type_name ;
  10 signal types:
    BIT,
    BIT_VECTOR,
    STD_LOGIC,
    STD_LOGIC_VECTOR,
    STD_ULOGIC,
    SIGNED,
    UNSIGNED,
    INTEGER,
    ENUMERATION,
    and BOOLEAN.
    SIGNAL x1 : BIT;
    SIGNAL C : BIT_VECTOR (1 TO 4) ;
    SIGNAL Byte : BIT_VECTOR (7 DOWNTO 0) ;

## Slide 21: VHDL operators (page 787)

## Slide 22: Example 1
f= ab
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
entity eg1 is
( a,b: in std_logic;
f: out std_logic
);
end eg1;
architecture logic_function of eg1 is
begin
f<= a and b;
end logic_function;