## Slide 1: VHDL example codes
Dr Tin Thet Nwe

## Slide 2: number systems
Decimal | Binary | Octal | Hexadecimal
0 | 0000 | 000 | 0000
1 | 0001 | 001 | 0001
2 | 0010 | 010 | 0010
3 | 0011 | 011 | 0011
4 | 0100 | 100 | 0100
5 | 0101 | 101 | 0101
6 | 0110 | 110 | 0110
7 | 0111 | 111 | 0111
8 | 1000 | 001 000 (10) | 1000
9 | 1001 | 001 001 (11) | 1001 (A)
10 | 1010 | 001 010 (12) | 1010 (B)
11 | 1011 | 001 011 (13) | 1011(C)
12 | 1100 | 001 100 (14) | 1100 (C)
13 | 1101 | 001 101 (15) | 1101(D)
14 | 1110 | 001 110 (16) | 1110€
15 | 1111 | 001 111 (17) | 1111(F)
16 | 10000 | 010 000 (20 ) | 0001 0000(10)
17 | 10001 | 011 001 (21) | 0001 0001(11)

## Slide 3: unsigned numbers
only positive numbers
8-bit unsigned numbers
  00000000 t0 11111111
  0 to 255

## Slide 4: signed numbers
both positive numbers and negative numbers
Most significant bit  sign bit

## Slide 5: signed number system
Sign-and-MagnitudeRepresentation
1’sComplementRepresentation
2’sComplementRepresentation
Sign-and-Magnitude (3-bit) | 1’sComplement (3-bit) | 2’sComplement (3-bit)
011 (+3) | 011 (+3) | 011 (+3)
010 (+2) | 010 (+2) | 010 (+2)
001 (+1) | 001 (+1) | 001 (+1)
000 (+0) | 000 (+0) | 000 (+0)
100 (-0) | 100 (-3) | 100 (-4)
101 (-1) | 101 (-2) | 101 (-3)
110 (-2) | 110 (-1) | 110 (-2)
111 (-3) | 111 (-0) | 111 (-1)

## Slide 6: 2’s complement system (signed addition)

## Slide 7: unsigned addition
4-bit + 4-bit  maximum 5 bit
15+15 = 30 (decimal)
1111 + 1111 = 1 1110 (binary)
8-bit + 8-bit  maximum 9-bit
11111111 + 11111111 = 1 1111 1110 (binary)
255 + 255 = 510 (decimal)

## Slide 8: fast adders
half adder ( 1-bit unsigned adder)
0 + 0 = 0(carry) 0 (sum)
0 + 1 = 0 1
1 + 0 = 0 1
1 + 1 = 1 0
full adder (3-bit unsigned adder)
  0 + 0+ 0 = carry(0) sum (0)
  1+ 1+ 1 = carry (1) sum (1)

## Slide 9: multiplier (unsigned)
4-bit x 4-bit = 8-bit (maximum)
1111 x 1111 = 11100001 (binary)
15 x 15 = 225
8-bit x 8-bit = 16-bit (maximum)
1111 1111 x 1111 1111 = 1111111000000001
255 x 255 = 650 25

## Slide 10
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
entity eg2 is
( A,B: in std_logic;
F: out std_logic;
);
end eg2;
architecture logic_function of eg2 is
begin
F<= (A and B) or ( (not A) and B );
end logic_function;

## Slide 11
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
entity eg2 is
( a,b: in std_logic;
f: out std_logic;
);
end eg2;
architecture logic_function of eg2 is
signal s1,s2,s3: std_logic;
begin
s1 <= a and b;
s2 <= not a;
s3 <= s2 and b;
f <= s1 or s3;
end logic_function;

## Slide 12: Write vhdl code for the following functions.

## Slide 13: Simple Signal Assignment
signal_name <=expression ;
For example,
a<= ‘1’;
b<= a and c;
b <= ‘1’ & a; ( b=5 bit , a = 4 bit )
(concatenate operator,&,)

## Slide 14: Assigning Signal Values Using OTHERS
S<=(OTHERS=>’0’) ; is equal to s <= “0000”;

## Slide 15: Selected Signal Assignment
with … select
when …..
when others…
For example,
with sel select
f<= ‘1’ when ‘1’
‘0’ when others;
Others may be 0,Z,-

## Slide 16: Conditional Signal Assignment
signal_name<= expressionWHEN logic_expressionELSE
expression ;
An example is
f <= ’1’WHEN x1=x2 ELSE
’0’ ;

## Slide 17: GENERATE Statement
the FOR GENERATE and the IF GENERATE.
generate label:
FOR index variable IN range GENERATE
statement ;
{statement ;}
END GENERATE ;
generate label:
IF expression GENERATE
statement ;
{statement ;}
END GENERATE ;

## Slide 18: sequential assignment statements
two types
  if-then-else statements
  case statements
VHDL requires that the sequential assignment statements be placed inside another type of statement, called a process statement.
PROCESS (w0, w1, s )
BEGIN
IF S=‘1’ THEN
F <= W0;
ELSE
F <= W1;
ENDIF ;
ENDPROCESS ;

## Slide 19: if-then-else statement
PROCESS (w0, w1, s )
BEGIN
IF S=“00” THEN
F <= W0;
ELSIF S=“01” THEN
F <= W1;
ELSIF S=“10” THEN
F <= W2;
ELSE
F<= W3;
ENDIF ;
ENDPROCESS ;

## Slide 20: case statement
PROCESS ( bcd )
  BEGIN
  CASE bcd IS - - abcdefg
      WHEN”0000” > leds<=”1111110” ;
      WHEN”0001” > leds<=”0110000” ;
      WHEN”0010” > leds<=”1101101” ;
      WHEN”0011” > leds<=”1111001” ;
      WHEN”0100” > leds<=”0110011” ;
      WHEN”0101” > leds<=”1011011” ;
      WHEN”0110” > leds<=”1011111” ;
      WHEN”0111” > leds<=”1110000” ;
      WHEN”1000” > leds<=”1111111” ;
      WHEN”1001” > leds<=”1110011” ;
      WHEN OTHERS> leds<=”-------” ;
  ENDCASE ;
ENDPROCESS ;

## Slide 21: Write a vhdl code for half adder named ha entity using logical operators.
half adder
x | 0 | 0 | 1 | 1
+y | 0 | 1 | 0 | 1
c s | 0 0 | 0 1 | 0 1 | 1 0
Inputs | Outputs carry sum | 
0 0 | 0 | 0
0 1 | 0 | 1
1 0 | 0 | 1
1 1 | 1 | 0

## Slide 22
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
entity ha is
Port ( a : in STD_LOGIC;
b : in STD_LOGIC;
c : out STD_LOGIC;
s: out STD_LOGIC);
end ha;
architecture Behavioral of ha is
begin
c <= a and b;
s <= a xor b;
end Behavioral;

## Slide 23: Subcircuts
AVHDL entity deﬁned in one source code file can be used as a subcircuit in another source code ﬁle.

## Slide 24: Seven segment display
Using a selected signal assignment, write VHDL code for seven segment display showing ‘0’ or ‘1’ using hex_to_sevenseg entity name.

## Slide 25
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
entity hex_to_sevenseg is Port ( data : in STD_LOGIC; seg : out STD_LOGIC_VECTOR (6 downto 0) ); end hex_to_sevenseg; architecture Behavioral of hex_to_sevenseg is begin with data select seg <= "1000000" when ‘0’ , "1111001" when ‘1’ , "11111111" when others; end Behavioral;

## Slide 26
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
entity hex_to_sevenseg is Port ( data : in STD_LOGIC_VECTOR (3 downto 0); seg : out STD_LOGIC_VECTOR (6 downto 0) ); end hex_to_sevenseg; architecture Behavioral of hex_to_sevenseg is begin with data select seg <= "1000000" when "0000" , "1111001" when "0001" , “0100100" when "0010" , "0110000" when "0011" , "0011001" when "0100" , "0010010" when "0101" , "0000010" when "0110" , "1111000" when "0111" , "0000000" when "1000" , "0010000" when "1001" , "11111111" when others; end Behavioral;

## Slide 27: VHDL code that display the half adder output on seven segment display
Create a VHDL entity named sevenseg that displays ‘0’ or ‘1’ on display . Create a second entity named logic that represents 3 1-bit input and 1 1-bit output. Create a third entity named main using one instance of the sevenseg entity and one instance of the logic entity. Include AN pins that controls the 8 seven segments on Nexys4 DDR board.